SECTION 12 2113

HORIZONTAL LOUVER BLINDS

This section includes editing notes to assist the user in editing the section to suit project requirements. These notes are included as hidden text, and can be revealed or hidden by one of the following methods:

Microsoft Word 2007: Click the OFFICE button, select WORD OPTIONS, select DISPLAY, then select or deselect the HIDDEN TEXT option.

Microsoft Word (earlier versions): From the pull-down menus select TOOLS, then OPTIONS. Under the tab labeled VIEW, select or deselect the HIDDEN TEXT option.

Corel WordPerfect: From the pull-down menus select VIEW, then select or deselect the HIDDEN TEXT option.

This master specification section has been prepared by Lutron Electronics Company, Inc. for use in the preparation of a project specification section covering wood or aluminum horizontal louver blinds with Sivoia QS electronic drive.

The following should be noted in using this specification:

Hypertext links to specific websites are included after manufacturer names and names of organizations whose standards are referenced within the text, to assist in product selection and further research. Hypertext links are contained in parenthesis and shown in blue, e.g.:

(www.astm.org)

Optional text requiring a selection by the user is enclosed within brackets, e.g.:  "Section [09 0000.] [_____.]"

Items requiring user input are enclosed within brackets, e.g.:  "Section [_____ - ________]."

Optional paragraphs are separated by an "OR" statement, e.g.:

**** OR ****

For assistance on the use of the products in this section, contact Lutron Electronics Company, Inc. by calling (800) 523-9466 or visit their website at www.lutron.com.

PART 1	GENERAL

1.1	SUMMARY

Edit the following paragraphs to include only those items specified in this section.

A.	Section Includes:

1.	Horizontal slat louver blinds.

2.	Operating hardware.

Coordinate the following paragraphs with other sections in the project manual.

B.	Related Sections:

1.	Division 01: Administrative, procedural, and temporary work requirements.

1.2	REFERENCES

A.	National Fire Protection Association (NFPA) (www.nfpa.org) 70 - National Electrical Code.

1.3	SUBMITTALS

Limiting submittals to only those actually required helps to minimize liability arising from the review of submittals. Minimize submittals on smaller, less complex projects.

Include the following for submission of shop drawings, product data, and samples for the Architect's review.

A.	Submittals for Review:

1.	Shop Drawings: Indicate blind locations, opening sizes, window depth, mounting type, return depth, locations of window operating hardware, power supply locations, and wiring diagrams.

2.	Product Data: Describe blind construction and finishes for slats, headrails, and accessories.

3.	Samples: [8] [__] inch long slat samples [showing available colors.] [in each color.]

B.	Closeout Submittals:

1.	Operation and Maintenance Data: Provide wiring diagrams, system control description, operational requirements, and reprogramming information.

1.4	QUALITY ASSURANCE

A.	Manufacturer Qualifications:

1.	Minimum 5 years experience in manufacture of low-voltage motorized systems.

2.	Provide single source for blinds and control systems.

B.	Installer Qualifications: Qualified by factory training and previous experience to install and commission specified products.

C.	Perform work in accordance with NFPA 70.

Include the following for full size mockups for review of construction, coordination of work of several sections, testing, and observation of operation. Minimum mockup dimensions are 24 inches wide x 12 inches high.

D.	Mockup:

1.	Provide mockup of one typical blind.

2.	Include blind, electrical connections, and controls.

3.	Locate [where directed.] [____.]

4.	Demonstrate operation throughout all cycles.

5.	Approved mockup may remain as part of the Work.

1.5	PROJECT CONDITIONS

A.	Do not install blinds until painting and finishing work is complete.

1.6	WARRANTIES

A.	Furnish manufacturer’s warranty providing coverage for repair or replacement of defective components up to following amounts:

1.	Up to 5 years after date of Substantial Completion: 100 percent of cost of replacement parts.

2.	5 to 8 years after date of Substantial Completion: 50 percent of cost of replacement parts.

1.7	MAINTENANCE

A.	Manufacturer:

1.	Provide 24-hour, 7-day technical support for troubleshooting and programming.

2.	Make replacement parts available for minimum of 10 years after date of manufacture.

PART 2	PRODUCTS

2.1	MANUFACTURERS

A.	Contract Documents are based on Lutron Venetian Blind with Intelligent Tilt Alignment  by Lutron Electronics Co., Inc.

Edit the following to indicate whether or not substitutions will be permitted for the products in this section.

B.	Substitutions: [Under provisions of Division 01.] [Not permitted.]

2.2	COMPONENTS - BLINDS

Include the following for aluminum blinds.

A.	Louver Slats: 2 inches wide, prefinished 0.008 inch thick aluminum horizontal slats with radiused corners.

**** OR ****

Include the following for Premium wood slats.

B.	Louver Slats:

1.	2 inches wide, solid wood horizontal slats, rectangular with square corners, ends finished to match slat finish.

Include the following for Elite Wood slats; edit to indicate desired wood species.

2.	Wood Species: [Cherry.] [Mahogany.] [Oak.] [Pine.] [Natural Hardwood.]

Include the following for factory fire-retardant treatment.

3.	Apply fire-retardant treatment.

Edit the following to indicate desired type of slat supports. Refer to current Lutron technical data for available decorative tape style.

C.	Slat Support: [Woven thin ladders.] [Wide decorative tapes, [____] style.

D.	Head Rail:

1.	2.25 inches deep x 3.75 inches tall.

2.	Prefinished extruded aluminum channel, internally fitted for hardware required for motorized blind operation.

In the following paragraph select steel for aluminum blinds and wood for wood blinds.

E.	Bottom Rail: [Prefinished rolled steel, with color-coordinated end caps.] [Solid wood, species to match louver slats.]

F.	Cord: Color coordinated to slat material and finish.

G.	Support Brackets: Suitable for wall, ceiling, or jamb mounting, formed steel, shaped to match head rail, allowing removal of head rail without removing bracket.

In the following paragraph, include returns for outside-mounted blinds; inside-mount blinds are furnished without returns.

H.	Valance: Material to match louver slats, [with returns to match headrail depth.] [to [__] inch depth.]

2.3	COMPONENTS - DRIVE UNITS

A.	System Description:

1.	Ultra-quiet, precision-controlled electronic drive unit housed inside head rail, independently controlling blind lift and tilt.

2.	Audible noise: Maximum 44 dBA measured 3 feet from electronic drive unit.

3.	Allow for maximum of 100 device interfaces including blinds, keypads, lighting controls, and power supplies.

4.	Allow for 100 zones including blinds and lighting zones.

B.	Power Requirements:

1.	24 VDC input provided by approved NEC Class 2 power source.

2.	One power supply output per electronic drive unit.

3.	Each electronic drive unit powers one blind.

C.	System Performance:

1.	One-touch control of blinds by means of keypad, lighting control, infrared remote, or RF remote.

2.	Capable of stopping bottom rail within accuracy of 0.125 inch at any point between open and close limits.

3.	Capable of rotating slats to minimum of 60 tilt positions.

4.	Capable of aligning tilt to within 1/16 inch of adjacent blinds.

5.	Store preset lift and tilt positions at any stop point along travel along with full open and full close limits for lift and tilt.

6.	Presets set by 5-second button push and hold from keypad, or lighting control.

7.	Move bottom rail of adjacent blinds with different electronic drive units in unison and alignment within 0.125 inch.

8.	Open and close limits programmable from electronic drive unit, keypad, lighting control, or handheld remote control for lift.

9.	Power failure memory.

10.	System components electro static discharge protected.

11.	Tilt control capable of electronic adjustment to limit tilt range for specific applications.

D.	Grouping:

1.	Keypads can control any electronic drive unit, group, or subgroup, or additional interface.

2.	System groups and subgroups configured at point of control without rewiring and without access to electronic drive unit.

3.	System may contain multiple electronic drive units.

4.	Controls able to operate any group or subgroup of electronic drive units regardless of window treatment type.

E.	Integration:

1.	Electronic drive units integrate with lighting controls without separate interface.

2.	Contact closure, R232, and Ethernet interfaces available to interface with audio/visual equipment and security systems.

F.	System Controls:

1.	Blinds controlled by built-in blind columns on lighting control or by keypad.

2.	Electronic drive units,  keypads, and lighting controls contain microprocessors, allowing high level programming from any source.

3.	Blinds, lighting controls, and keypads wired together on same communications link.

Include the following for a Hyperion solar adaptive control, accessed through optional blind monitor and control license.

G.	Open Loop Solar Adaptive Algorithm:

1.	Design system to:

a.	Optimize daylight.

b.	Provide manual override capability for occupants via wall mounted keypad or simple remote control.

c.	Maximize occupants connectivity with outdoors by optimizing view.

d.	Provide diffuse daylight and minimize direct sunlight in the space to reduce solar heat gain and maximize occupants’ comfort in space.

e.	Reduce glare.

f.	Start, stop, and track blinds along same facade in unison for both lift and tilt.

g.	Independently control and adjust lift and tilt.

2.	Hardware: Independent operation of solar tracking program through non-Windows based operating system provided in one or more light management panels.

3.	Control software:

a.	Calculates sun’s position in sky relative to building, then calculates when blind movement is necessary, by facade.

b.	Calculates position of blind to limit direct sunlight penetration to predetermined limit.

4.	Use following inputs for start up:

a.	Building location.

b.	Facade orientation.

c.	Window dimensions.

d.	Solar depth of penetration

e.	Number of blind movements per day.

5.	Do not require user to make daily changes to programming or overall system functionality unless desired.

6.	User interface:

a.	PC graphic user interface: Provide access to adjustable parameters of solar depth of penetration and number of blind movements per day.

b.	Manual override:

1)	Temporary override of control program available through optional manual keypads.

2)	Keypads capable of providing manual control of blinds in particular area, with independent control for lift and tilt.

2.4	CONTROLS AND ACCESSORIES

A.	Wall Mounted Controls:

1.	Low voltage keypads:

a.	Electronically set and reconfigure blind open and close limits for lift, blind preset positions for lift, system groups, and system subgroups without rewiring or access to electronic drive unit.

b.	Fit into standard electrical box.

2.	Face plates:

a.	Attach without visible means of attachment.

b.	Engraved artwork.

3.	Product color: Match NEMA WD1.

4.	Provide immediate local LED response upon button activation.

5.	Backlit buttons.

6.	Removable button assemblies allowing field changes.

7.	Capable of simultaneously controlling one or more blinds.

Edit the following to indicate desired types of controls.

8.	Type: [Two button.] [Three button.] [Three button with tilt.] [Four button with tilt and infrared reception.] [Four button for dual mount or two group applications.] [Six button for dual mount or two group applications.] [Five button with tilt.] [Multi-group keypad for control of multiple groups of blinds.]

B.	Infrared Receivers:

1.	Available on system keypads, as attachment to electronic drive unit, or on system contact closure input board.

2.	Electronically set and reconfigure blind open and close lift limits, blind lift preset points, system groups, and system subgroups without rewiring and without access to electronic drive unit.

3.	Include circuitry to reduce degraded performance.

Edit the following to indicate desired types of controls.

4.	Type: [Open/close handheld transmitter.] [Open/preset/close handheld transmitter.] [Three preset handheld transmitter.] [Multi-function handheld transmitter.] [Dual group open/preset/close handheld transmitter.]

C.	Handheld Remotes: Lutron Sivoia QS Hand-Held Infrared Transmitter.

**** OR ****

D.	Handheld Remotes: Lutron Hand-Held RF Transmitter.

Edit the following to indicate desired types of interfaces.

E.	Infrared Interfaces:

1.	Interface to other control system via dry contact closure input device.

2.	Interface with Lutron GRAFIK Eye System.

F.	Transformers:

1.	Electronic drive units powered with 24 VDC power supply; power supplied via NEC Class 2 power source.

Edit the following to indicate desired type of transformers.

2.	Provide [individual power supply for each electronic drive unit.] [power panel including 10 individual power supplies.]

2.5	FABRICATION

A.	Fabricate blinds to fit openings with uniform edge clearance of 1/4 inch.

B.	At openings requiring multiple blind units, provide separate blind assemblies with space of 1/2 inch between assemblies, occurring at window mullion centers.

2.6	FINISHES

Include the following for aluminum slats; edit to indicate desired colors.

A.	Louver Slats: Manufacturer’s standard brushed finish or baked enamel, [____] color [to be selected from manufacturer's full color range].

**** OR ****

Include the following for Premium wood slats; edit to indicate desired finish and colors.

B.	Louver Slats: Manufacturer’s standard [stained finish,] [painted finish,] [____] color [to be selected from manufacturer's standards].

**** OR ****

Include the following for Elite wood slats; edit to indicate desired finish and colors.

C.	Louver Slats: [Manufacturer’s standard clear finish.] [Custom finish to match Customer-supplied sample].

D.	Head Rails and Brackets: Color coordinated to louver slats.

E.	Bottom Rail: Finish to match slats.

In the following paragraph, color to match louver slats is standard; colors different than louver slats is an optional upgrade.

F.	Ladders and Cords: [Color coordinated to louver slats.] [[____] color [to be selected from manufacturer's standards.]

G.	Tapes: [[____] color [to be selected from manufacturer's standards.]

In the following paragraph, color to match louver slats is standard; colors different than louver slats is an optional upgrade.

H.	Valance: [Finish to match louver slats.] [[____] finish [to be selected from manufacturer's standards.]

PART 3	EXECUTION

3.1	INSTALLATION

A.	Install blinds in accordance with manufacturer's instructions.

B.	Secure with concealed fasteners.

C.	Installation Tolerances:

1.	Maximum gap at window opening perimeter: 1/4 inch.

2.	Maximum offset from level: 1/8 inch.

3.2	ADJUSTING

A.	Adjust blinds for smooth operation and to clear window operating hardware.

3.3	DEMONSTRATION

A.	Demonstrate proper operation and maintenance of blinds to Owner.

END OF SECTION